## Slide 1: Multisector modeling of critical minerals and materials using GCAM
Yang Qiu, Brinda Yarlagadda, Gokul Iyer, Neal Graham, Matthew Binsted, Marshall Wise, Pralit Patel, Allen Fawcett
Pacific Northwest National Laboratory,
Joint Global Change Research Institute
2025 GCAM Annual Meeting
June 3, 2025

## Slide 2: Multisector CMM modeling in GCAM: our philosophy
Our goal is to represent CMM demands, supplies and trade endogenously within GCAM (rather than with ex-post calculations) to capture the multisectoral interactions between material markets and technology deployment in various sectors of the economy

## Slide 3: Key structural changes to model CMM demand in GCAM
1. Sectoral and material coverage – represent a list of 13 CMMs across multiple sectors (with flexibility to expand to other CMMs and sectors if needed).

## Slide 4: Key structural changes to model CMM demand in GCAM
1. Sectoral and material coverage – represent a list of 13 CMMs across multiple sectors (with flexibility to expand to other CMMs and sectors if needed).
2. Technology cost structure modification – separate technology capital cost into material cost and non-material capital cost.

## Slide 5: Key structural changes to model CMM demand in GCAM
1. Sectoral and material coverage – represent a list of 13 CMMs across multiple sectors (with flexibility to expand to other CMMs and sectors if needed).
2. Technology cost structure modification – separate technology capital cost into material cost and non-material capital cost.
3. Adding subtype technologies – represent material demand more accurately and allow technology and material substitution.

## Slide 6: GCAM results on multisector material demand (US result as an example)

## Slide 7
Research questions: how does different energy sectors respond and interact under potential material supply constraints?
Material supply could be affected by various factors:
Resource availability;
Mining lead times;
Geopolitical issues;
Trade barriers
In our initial experiment, we developed exogenous constraints on global annual copper supply using detailed data on mining projects development stages and lead times.
(S&P global)
Initial experiment to explore multisectoral implications under the material supply scarcity or constraint

## Slide 8: Initial experiment to explore multisectoral implications under the material supply scarcity or constraint
No_constraint – future Cu supply is unlimited.
Cu supply constraint – future annual Cu availability constrained based on assumptions about lead time of each mining stage
Annual Cu availability constraint
Electricity generation
Electricity T&D
H2 production
Transport
No constraint
Cu supply constraint
Difference
Under the Cu supply constraint, Cu demand reduces across these sectors. The extent of the reduction depends on the relative copper intensity of the technologies within each sector.

## Slide 9: Initial experiment to explore multisectoral implications under the material supply scarcity or constraint
Differences relative to No constraint
An exogenous constraint on annual copper availability has the following effects:
Higher cost of battery electric vehicles (BEVs) – A Cu constraint makes BEVs more expensive as BEVs have higher Cu intensity than internal combustion engine vehicles, resulting in reduced BEV deployment. Concurrently, deployment of internal combustion engine vehicles increases.
Cu supply constraint
Global transport service output (cars)
Less service output of BEV
BEV with different battery types

## Slide 10: Initial experiment to explore multisectoral implications under the material supply scarcity or constraint
An exogenous constraint on annual copper availability has the following effects:
Higher cost of battery electric vehicles (BEVs) – A Cu constraint makes BEVs more expensive as BEVs have higher Cu intensity than internal combustion engine vehicles, resulting in reduced BEV deployment. Concurrently, deployment of internal combustion engine vehicles increases.
Higher electricity price – A Cu supply constraint results in higher costs of electricity generation and T&D since Cu is demanded in all electricity generation technologies as well as transmission and distribution infrastructures.
Differences relative to No constraint
Electricity price (US as an example)
Cu supply constraint
Cu supply constraint
Differences relative to No constraint
Global electricity generation
Higher electricity price

## Slide 11: Work in progress: regional resource supply curve implementation
Example: Copper supply in USA
We represent material supply with a layered supply curve approach:
Cumulative resource supply curve – the relationship between extraction cost and cumulative quantity of resource being extracted.
Annual production constraint – the rate at which material production capacity can grow over time.

## Slide 12: Work in progress: regional resource supply curve implementation
Source: gcamdata processing of S&P Global mine-level data
Supply curve data of GCAM regions: We are using mine-level data of project lead times, resource availability, and extraction costs to represent long-term resource supply curves and annual production capacity constraints at GCAM 32-region level.
Lithium annual production limit (Mt/yr)
Lithium resource supply (Mt)