## Slide 1: Implications of AI and data center service demand on energy, water, and economic systems
Stephanie Morris, Tom Wild, Mengqi Zhao, Pralit Patel, Marshall Wise
GCAM Annual Meeting
3 June 2025

## Slide 2: Growing importance and multisectoral impacts of data centers
Rapid expansion in demands for data center services – AI, cloud computing, storage, etc.
Changing demands for DC services
  2024: cloud computing 54%, traditional workloads 32%, AI 14%
  2027: cloud 50%, AI 27%, traditional workloads 23%
Resource intensity
  Electricity: 1% global electricity – average data center ~5-10 megawatts (MW), hyperscale ~100+ MW
  U.S. electricity consumption >doubled, 2017-2023
  Water (quantity, quality): <0.2% of U.S. withdrawals
  Critical materials
  Land
  Emissions
  Economy (capital investment, jobs, energy expenditures): Annual investment in construction doubled in the US from 2023-2024, 0.5% of US GDP
Local impacts are likely to be more pronounced, as DCs tend to be spatially concentrated
  Projected to be 6.7-12% of total U.S. electricity in 2028
  5 US states > 10% of electricity consumption, Virginia > 25%
Lawrence Berkeley National Laboratory. 2024 United States Data Center Energy Usage Report. 2024.

## Slide 3: Growing importance and multisectoral impacts of data centers
Rapid expansion in demands for data center services – AI, cloud computing, storage, etc.
Changing demands for DC services
  2024: cloud computing 54%, traditional workloads 32%, AI 14%
  2027: cloud 50%, AI 27%, traditional workloads 23%
Resource intensity
  Electricity: 1% global electricity – average data center ~5-10 megawatts (MW), hyperscale ~100+ MW
  U.S. electricity consumption >doubled, 2017-2023
  Water (quantity, quality): <0.2% of U.S. withdrawals
  Critical materials
  Land
  Emissions
  Economy (capital investment, jobs, energy expenditures): Annual investment in construction doubled in the US from 2023-2024, 0.5% of US GDP
Local impacts are likely to be more pronounced, as DCs tend to be spatially concentrated
  Projected to be 6.7-12% of total U.S. electricity in 2028
  5 US states > 10% of electricity consumption, Virginia > 25%
Lawrence Berkeley National Laboratory. 2024 United States Data Center Energy Usage Report. 2024.

## Slide 4: Growing importance and multisectoral impacts of data centers
Rapid expansion in demands for data center services – AI, cloud computing, storage, etc.
Changing demands for DC services
  2024: cloud computing 54%, traditional workloads 32%, AI 14%
  2027: cloud 50%, AI 27%, traditional workloads 23%
Resource intensity
  Electricity: 1% global electricity – average data center ~5-10 megawatts (MW), hyperscale ~100+ MW
  U.S. electricity consumption >doubled, 2017-2023
  Water (quantity, quality): <0.2% of U.S. withdrawals
  Critical materials
  Land
  Emissions
  Economy (capital investment, jobs, energy expenditures): Annual investment in construction doubled in the US from 2023-2024, 0.5% of US GDP
Local impacts are likely to be more pronounced, as DCs tend to be spatially concentrated
  Projected to be 6.7-12% of total U.S. electricity in 2028
  In 2023, 5 US states > 10% of electricity consumption and Virginia > 25%
Datacentermap.com
Datacentermap.com

## Slide 5: Comprehensive analysis of the impact of data centers is a quintessential MSD use case
GCIMS focus on understanding future energy, water, land, and economic implications of expanded demand for data center services, in the U.S. and internationally
Research questions cross spatial scales
Cutting-edge research bringing together DOE Office of Science-funded capabilities
Building on many years of multisector dynamics research

## Slide 6: GCIMS approach to analyzing the future of energy, water, and economic implications of data centers
Data centers exist to provide services
  Storage, streaming
  Cloud, HPC, AI
Different types of DCs to provide different services, with differing resource use intensities
  Co-located/traditional
  Hyperscale
DCs require electricity, water, land, and critical minerals
  Competition with other demands: residential, industry, municipal, transportation, agriculture
DC services feedback to the economy through labor productivity, jobs

## Slide 7: GCIMS approach to analyzing the future of energy, water, and economic implications of data centers
Data centers exist to provide services
  Storage, streaming
  Cloud, HPC, AI
DC services feedback to the economy through labor productivity, jobs
Different types of DCs to provide different services, with differing resource use intensities
  Co-located/traditional
  Hyperscale
DCs require electricity, water, land, and critical minerals
  Competition with other demands: residential, industry, municipal, transportation, agriculture

## Slide 8: GCIMS approach to analyzing the future of energy, water, and economic implications of data centers
Data centers exist to provide services
  Storage, streaming
  Cloud, HPC, AI
DC services feedback to the economy through labor productivity, jobs
Different types of DCs to provide different services
  Co-located/traditional
  Hyperscale
DCs require electricity, water, land, and critical minerals
  Competition with other demands: residential, industry, municipal, transportation, agriculture

## Slide 9: GCIMS approach to analyzing the future of energy, water, and economic implications of data centers
Data centers exist to provide services
  Storage, streaming
  Cloud, HPC, AI
DC services feedback to the economy through labor productivity, jobs
Different types of DCs to provide different services
  Co-located/traditional
  Hyperscale
DCs require electricity, water, land, and critical minerals
  Differing resource use intensities for hyperscale vs. traditional DCs
  Competition with other demands: residential, industry, municipal, transportation, agriculture

## Slide 10: GCAM represents multiple services, technologies, and data center building types
Data center services (TFLOP)
  Email, storage
  Cloud computing
  AI (development, training, inference)
Data center building types (m2)
  Traditional
  Hyperscale
IT technologies
  Service efficiency (EJ/TFLOP)
  Cost ($/TFLOP)
  Cooling requirements
Cooling technologies
  Water (km3)
  Energy (EJ)
  Cost ($)

## Slide 11: Research gap
Demand for data center services and facilities will change in the coming years, with implications for multiple sectors, both in competition for resources and potential feedbacks to the economy. he growth of data centers?

## Slide 12: Research questions
What are the key processes, drivers, and uncertainties impacting the future growth of data center services and data center expansion?
What effects could AI have on economic growth, through changes in sectoral and feedbacks to labor productivity?
How will electricity, water, and land systems be impacted by DC/AI expansion?
What physical constraints might limit the growth of data centers?

## Slide 13: Research questions
What are the key processes, drivers, and uncertainties impacting the future growth of data center services and data center expansion?
What effects could AI have on the economy, through changes in sectoral composition and feedbacks to labor productivity?
How will electricity, water, and land systems be impacted by DC/AI expansion?
What physical constraints might limit the growth of data centers?

## Slide 14: Research questions
What are the key processes, drivers, and uncertainties impacting the future growth of data center services and data center expansion?
What effects could AI have on the economy, through changes in sectoral composition and feedbacks to labor productivity?
How will electricity, water, and land systems be impacted by DC/AI expansion?
What physical constraints might limit the growth of data centers?

## Slide 15: Research questions
What are the key processes, drivers, and uncertainties impacting the future growth of data center services and data center expansion?
What effects could AI have on the economy, through changes in sectoral composition and feedbacks to labor productivity?
How will electricity, water, and land systems be impacted by DC/AI expansion?
What physical and societal constraints might limit the growth of data centers, such as water scarcity or siting decisions?

## Slide 16
GCAM scenarios

## Slide 17: GCAM analysis: scenario design
Model parameter | Description (Low/High)
Service demand (TFLOP) | Slower/faster demand growth rate for services (AI, cloud, traditional)
Service efficiency (EJ/TFLOP) | Slower/faster improvement rate for IT equipment energy per unit of service
Power Use Effectiveness | Slower/faster rate of improvement in PUE (total DC electricity per unit of IT electricity)
Water Use Effectiveness (L/kWh) | Slower/faster rate of improvement in WUE (water usage per unit of IT electricity)
Reference | Current trends across all four parameters
U.S. total DC electricity demand projections

## Slide 18: GCAM analysis: 2025 state-level data center electricity demand
2025 data center electricity demand
Historical
Projection
Virginia data center electricity demand

## Slide 19: GCAM analysis: uncertain growth for data center electricity demand
Historical
Projection
Reference
2060 data center electricity demand,
Reference scenario
~5x
Virginia data center electricity demand scenario projections

## Slide 20: GCAM analysis: uneven impacts across the U.S. for DC electricity share of total demand
Historical
Projection
Reference
2025 data center share of total state electricity
Virginia data center share electricity

## Slide 21: GCAM analysis: share of electricity demand for DCs could exceed 40% in multiple states and nearly 75% in Virginia
Historical
Projection
Reference
2060 data center share of total state electricity
Reference Scenario
Virginia data center share electricity scenario projections
~2x

## Slide 22: GCAM analysis: direct DC water use for cooling is currently <0.5% in all states – local shares are likely larger
2025 data center cooling water demand share of state consumption (direct only)
Virginia data center total cooling water demand (direct only)
Total = Direct (IT equipment and other DC cooling) + Indirect (cooling water for electricity generation)

## Slide 23: GCAM analysis: direct DC water use for cooling increases by less than total energy – hyperscale DCs tend to be more water efficient than traditional DCs
2060 cooling water demand share of state consumption (direct only), Reference Scenario
Virginia data center total cooling water demand (direct only)
~4x
Total = Direct (IT equipment and other DC cooling) + Indirect (cooling water for electricity generation)

## Slide 24: Next steps
These developments, combined with other MSD modeling capabilities, allows exploration of a range of relevant outcomes for data centers and the future implications of AI
Electricity – prices, household energy burden, grid operations, siting
Water – regional and high-resolution municipal water prices, use, scarcity, multi-sector tradeoffs, and groundwater depletion
Critical minerals and materials and land – resource extraction, prices, net trade, etc.
Economic development – GDP growth, jobs, net energy-economic impacts (accounting for resource usage and efficiency gains)

## Slide 25
GCIMS is supported by the U.S. Department of Energy, Office of Science, Earth and Environmental System Modeling, MultiSector Dynamics Program Area