## Slide 1
Exploring the Energy-Water Dynamics of Data Centers
Casey Burleyson, Kerem Ziya Akdemir, Kendall Mongird, Travis Thurber, and Jennie Rice

## Slide 2: Projections of new data centers to support generative AI and cryptomining are large but highly uncertain
Projections suggest up to a 15% annual growth in electricity demand from data centers within the next 5-10 years (EPRI 2024).
Usage projections from more recent AI models suggest electricity demand could be much lower than ChatGPT-type models.
Total electricity demand may grow 35-50% by 2040, driven by domestic manufacturing, data centers, and electrification (ACP 2025).
Data centers are also potentially large consumers of fresh water, depending on the cooling technology (Siddik et al. 2021).
2
“Drought-stricken communities push back against data centers”, 19-Jun 2021, NBC News

## Slide 3: Rapid, uncertain growth in electricity demand poses reliability challenges for the grid
3
“Electricity peak demand and energy growth forecasts over the 10-year assessment period continue to climb; demand growth is now higher than at any point in the past two decades. Increasing amounts of large commercial and industrial loads are connecting rapidly to the BPS. The size and speed with which data centers (including crypto and AI) can be constructed and connect to the grid presents unique challenges for demand forecasting and planning for system behavior.”
Primary drivers of demand growth

## Slide 4: Task 1 – Impacts of alternative scenarios of data center electricity demand growth on grid stress
Study Parameters | 
Time Horizon | 2025-2035
Spatial Resolution | Balancing Authorities
Key Assumptions (also modeled as sensitivities) | Growth rates of 3.71-15% annually No new generation explicitly to meet data center demand Data center hourly demand profiles are flat
Science Questions:
What is the projected impact (i.e., on electricity prices, reliability, etc.) of data centers on grid operations if grid infrastructure is built without considering these demands? Under what growth rates do the projected data center demands stress the grid?
How might delaying scheduled generator retirements lessen grid stress due to data centers?
What is the impact of treating some data center loads as interruptible demands? If their loads were modeled as appropriate for demand response participation, how does that added flexibility reduce stress on the grid?
4

## Slide 5: For now, projections of data center growth were sourced from the gray literature
5

## Slide 6: We are building from existing IM3 load projections
6
Burleyson et al. 2025: When do different scenarios of projected electricity demand start to meaningfully diverge? Applied Energy, 380, 124948, doi:10.1016/j.apenergy.2024.124948.

## Slide 7: Data centers significantly accelerate load growth in all three grid interconnections
7

## Slide 8: Data centers significantly accelerate load growth in all three grid interconnections
8
+25 GW (~15%) of needed capacity in 2035
25+ years of load growth compressed into a decade

## Slide 9: Data center growth leads to higher hourly electricity prices in the Western Interconnection
9
The effect of data center loads on electricity prices is relatively small in 2025 (+3-4%) and in 2030 (+5-12%).
Price divergence between different data center growth scenarios becomes clear in 2035.
Compared to the base scenario, yearly average electricity prices in 2035 increase 43%, 47%, 91%, and 202% under low, moderate, high, and higher data center load growth scenarios, respectively. This extreme increase is largely driven by data centers exacerbating the prices during worst (most expensive) 10-15 days of the year.

## Slide 10: Deferring scheduled generator retirements alleviates higher prices and unserved energy due to data centers
10

## Slide 11: Deferring scheduled generator retirements alleviates higher prices and unserved energy due to data centers
11

## Slide 12: Task 2 – Impacts of data center demands, siting, and configuration on water stress and grid stress
Study Parameters | 
Time Horizon | 2025-2055
Key Assumptions (also modeled as sensitivities) | New data centers matched 1:1 with new generation Generation can be co-located or off-site Cooling water demands depend on cooling technology/water availability
Science Questions:
Where, when, and to what extent do data centers contribute to water scarcity? Where and when does water availability constrain data center siting? What are the most important constraints for data center siting?
What is the impact on the grid and on water stress of relying on co-located generation versus remote (i.e., in the same interconnection but not the same site) generation to support data center demands?
12

## Slide 13: Approach to siting new data centers
Step 1: Conduct extensive review of data center developer documents and reports to determine common factors in location decision making and technology choices.
https://www.switch.com/switch-superloop/
https://datacenters.microsoft.com/wp-content/uploads/2023/05/Azure_Modern-Datacenter-Cooling_Infographic.pdf
https://www.cyrusone.com/data-centers/north-america/quincy-washington
Cooling Methods
https://sabeydatacenters.com/locations/quincy-data-center
Dry & Cool
13

## Slide 14
vs
Proprietary
Crowd-sourced
Step 2: Collect geospatial data of existing large scale data centers to spatially determine additional siting commonalities and validate siting suitability.
14
Approach to siting new data centers

## Slide 15: Virginia is for data centers
15

## Slide 16: Data centers are being built in many places, but tend to be clumped together
16
Data Sources: OpenStreetMap

## Slide 17: >97% of data centers are located within 1km of a high-speed fiber provider service territory
74% have access to at least two high speed fiber providers
Proximity to Fiber network
Data Sources: FCC Broadband Map, OpenStreetMap
17

## Slide 18: Having more direct access to reliable power sources is prioritized because service disruptions are costly
Cheap & reliable electricity
Data Sources: HIFLD, OpenStreetMap
76% of data centers are located within 1km of a substation
18

## Slide 19
Composite Siting Suitability + Existing Data Center Locations
NV
19
Our preliminary siting suitability is highly aligned with existing large data center locations
Data Sources: OpenStreetMap

## Slide 20: We are making the raw data publicly available
20

## Slide 21: Key results
Data centers significantly accelerate load growth in all three interconnections.
Compared to our base scenario with no data centers, annual average electricity prices in 2035 increase 43%, 47%, 91%, and 202% under the EPRI low, moderate, high, and higher data center load growth scenarios, respectively.
Postponing 100% of nuclear and 50% of natural gas planned retirements (≈22.6 GW) eliminates all price increases in 2035 due to data centers for the EPRI low, moderate, and high growth scenarios.
Data center locations are sensitive to electricity prices, access to water, access to multiple fiber provides, and proximity to substations.
21

## Slide 22: References
American Clean Power (ACP), 2025: US National Power Demand Study. https://cleanpower.org/resources/us-national-power-demand-study/.
Electric Power Research Institute (EPRI), 2024: Powering Intelligence: Analyzing Artificial Intelligence and Data Center Energy Consumption. https://www.epri.com/research/products/000000003002028905.
North American Electric Reliability Corporation (NERC), 2024: 2024 Long-Term Reliability Assessment. https://www.nerc.com/pa/RAPA/ra/Reliability%20Assessments%20DL/NERC_Long%20Term%20Reliability%20Assessment_2024.pdf.
Northwest Power and Conservation Council (NWPCC), 2024: Pacific Northwest Power Supply Adequacy Assessment for 2029. https://www.nwcouncil.org/reports/2024-4/.
Siddik, M. A. B., A. Shehabi, and L. Marston, 2021: The environmental footprint of data centers in the United States. Environ. Res. Lett., 16, 064017, doi:10.1088/1748-9326/abfba1.
Western Electricity Coordinating Council (WECC), 2024: An Assessment of Large Load Interconnection Risks in the Western Interconnection. https://www.wecc.org/wecc-document/19111.
22

## Slide 23: Backup Slides
23

## Slide 24: The impact of data center demand curtailment and/or demand shifting is limited
24