## Slide 1: Palladium Catalyst Breaks Strong Bonds, Leaving Weaker Ones Alone
Scientific Achievement
  Realized and identified a new pathway that cleaves the C-O bonds in aromatic ethers using Pd catalysts, breaking these bonds under mild conditions.
  Significance and Impact
  New pathway for converting lignocellulose into fuels, reducing the energy required.
  Research Details
  Achieved the cleavage of ether bonds by inserting water.
  By using 18O- labeled water, it was identified that the reaction occurs by partial hydrogenation of the aryl ring and addition of water to form an intermediate (hemiacetal) that rapidly eliminates phenol or alcohol.
  Unexpectedly, the catalyst cleaved the stronger aromatic C-O bond rather than cleaving the weaker alkyl bond.
  Palladium was far more selective than other catalysts, achieving up to 80% hydrolysis at complete conversion.
Pathways for the reductive hydrolysis of aryl ethers on palladium surfaces.
M Wang, et al.,
Angewandte Chemie Int. Ed., 56, 2017, 2110. DOI: 10.1002/anie.201611076
Meng Wang, Hui Shi, Donald M. Camaioni, and Johannes A. Lercher, PNNL
Notes: Using a palladium catalyst, Pacific Northwest National Laboratory scientists have identified reductive hydrolysis as a novel pathway for breaking carbon-oxygen bonds in aromatic ethers at relatively mild temperatures and pressures of hydrogen. Catalytic cleavage of these bonds via reductive hydrolysis could prove an effective way to enhance the production of fuels from waste lignocellulosic biomass.
-------------------
PI: Johannes A. Lercher
Project: 47319, KC0302010, Low-Temperature Catalytic Routes for Energy Carriers via Spatial and Chemical Organization
DOE Program Manager: Viviane Schwartz
Publication: Palladium-Catalyzed Hydrolytic Cleavage of Aromatic C−O Bonds
Meng Wang, Hui Shi, Donald M. Camaioni, and Johannes A. Lercher
dx.doi.org/10.1002/anie.201611076 | Angewandte Chemie International Edition